## Slide 1
A PERSONAL NETWORK-ANALYSIS ENGINE
netweevil
A local network-analysis engine I built for my own routing research.
It does not replace OSRM, Valhalla, pgRouting, or QNEAT3. Each of those is better at what it was built for. netweevil exists to solve a specific set of problems I kept running into.
Rust engine
HTTP API
QGIS plugin
Reproducible runs
Built on the shoulders of OpenStreetMap, the routing-research community, and decades of open-source GIS work.

## Slide 2
WHY I BUILT IT
A pile of recurring research questions
Across years of network-analysis work, the same kinds of requests kept coming back, and most were awkward to answer reproducibly:
“Route an ambulance, but trust nothing on bad surfaces.”
“Give me the same answer every time, and show how you got it.”
“Respect that no-left-turn-from-this-lane via-way restriction.”
“Pedestrian and bus together, as one journey.”
“Now simulate 600 cars in the morning peak and show the jams.”
WHY A NEW TOOL, NOT A FORK
Answering these in OSRM or Valhalla usually meant editing C++ or Lua and re-preprocessing. In pgRouting it meant a PostGIS stack and SQL per question. In QNEAT3 it meant waiting on Python Dijkstra.
All of those are reasonable. None gave me one workflow where every parameter stayed explainable and every run stayed reproducible for a paper.
netweevil
02 / 16

## Slide 3
WHAT IT IS
An analysis engine, not a production backend
A Rust-first local system for OSM routing research, reproducible analysis, transit experiments, and traffic simulation.
CLI
netweevil binary
Scriptable, deterministic, CI-friendly. Import, compile, analyze, simulate, report.
HTTP API
Axum service
Datasets and profiles held in memory. JSON or GeoJSON, ready for the plugin or a notebook.
QGIS PLUGIN
QGIS 3.28 to 4.99
Route, OD, matrix, service-area, transit and live simulation loaded as grouped layers.
REPORTS
Manifests and exports
Run manifests plus GeoJSON, CSV, GPKG, Parquet, GeoParquet you can defend later.
It is built to be an analysis engine for research and study work. You could run it behind an app, but that is not the goal. The goal is that every parameter is explainable and tunable, and the output is shaped to whatever a network analysis needs.
netweevil
03 / 16

## Slide 4
THE ROUTING CORE
Exact results at interactive speed
Many accelerators trade a little accuracy for speed. netweevil's edge-based Customizable Contraction Hierarchy returns the same route as a brute-force shortest path, checked route for route against my own exact engine.
No shortcut budgets. The hierarchy is built by a complete elimination game. Nothing is dropped to fit a memory cap, so exactness is preserved.
Per-direction termination. A correct bidirectional stopping rule for hierarchy search, with no silent under-search.
Restrictions survive. Turn and via-way restrictions are honoured, with an automaton A* fallback for the rare violating candidate.
GRONINGEN PROVINCE, 1.02M EDGE STATES
Median route latency
131
ms
→
2.9
ms
about 45x faster than my brute-force engine
p99 around 13 ms
Differential-identical summaries vs ground truth
netweevil
04 / 16

## Slide 5
COST MODELS
Cost models are data you can tune
Speeds, surface and smoothness factors, turn penalties, ferries, tolls, and preferences live in a plain YAML profile. Edit it, compile in seconds, route. No engine rebuild, so every parameter in a study stays visible and version-controlled.
car
ambulance
bicycle
pedestrian
plus rush-hour variants, or any mode you write
Same engine, different YAML.
The ambulance profile raises motorway speed and trusts tolls fully, then collapses speed on bad or impassable surfaces, written as rules a reviewer can read. A new mode for a one-off study is a file you can drop into a paper's appendix.
ambulance_emergency_call_v1.yml
speed_rules:
- match: { highway: motorway }
speed_kph: 150
factors:
- match: { surface: sand }
speed_factor: 0.25
- match: { smoothness: impassable }
speed_factor: 0.08
turns:
uturn_penalty_s: 12
preferences:
use_tolls: 1.0
returns:
explain_cost_derivation: true
netweevil
05 / 16

## Slide 6
DEFENSIBLE NUMBERS
Costs that explain themselves, output you shape
Turn on penalty_breakdown and explain_cost_derivation, and every second and metre is attributed back to where it came from. A returns block lets each request ask for exactly the columns the analysis needs.
✓
Road-type breakdown
Time and distance split across motorway, primary, residential, and so on.
✓
Surface breakdown
How much of the trip ran on cobblestone, gravel, or asphalt.
✓
Penalty breakdown
Left turns, U-turns, signals, roundabouts, each on its own line.
✓
You shape the return
Geometry none, full, or segments. Segment rows and breakdowns only when asked.
This is the reason netweevil exists. Results that survive peer review, where nobody has to take the router's word for anything.
netweevil
06 / 16

## Slide 7
ANALYSIS SUITE
A full network-analysis toolbox
Route
Single shortest path, with alternatives and full geometry.
Route-batch
Thousands of routes in one deterministic run.
OD
Origin to destination pairs from CSV or JSON.
Matrix
Many-to-many time and distance matrices.
Service area
Isochrones and reachable network from one or many origins.
Accessibility
Who-can-reach-what scoring across the network.
QGIS MAP PLACEHOLDER
Service-area isochrone from a city-centre origin: nested 5, 10, and 15-minute reachable polygons over the OSM street network.
FIG 7A
netweevil
07 / 16

## Slide 8
CORRECTNESS IN THE DETAILS
Turn restrictions, including the hard ones
Simple no-left-turns are easy. The ones that quietly break routers are via-way restrictions, where a manoeuvre is banned only along a specific approach and connector.
Multi-edge restriction sequences Modelled as ordered edge sequences, beyond single-node turns.
Validated against the accelerator The fast CCH candidate is checked against the restriction set.
Automaton A* fallback Used only when a candidate would violate a restriction, so exactness costs nothing elsewhere.
Signals and penalties Traffic-signal nodes and turn penalties fold straight into the cost.
QGIS MAP PLACEHOLDER
Two routes for the same origin and destination: the naive path takes an illegal via-way turn (red), and netweevil's legal detour (green). Annotate the restricted manoeuvre.
FIG 8A
netweevil
08 / 16

## Slide 9
MULTIMODAL
GTFS transit as part of the engine
Import a GTFS feed, set a service date, and route pedestrian and transit together as one journey. Walk to the stop, ride, transfer, walk to the door.
GTFS import Persisted transit bundles with explicit service-date windows.
Pedestrian and transit routing Walking access and egress stitched to scheduled services.
Transit service areas Time-of-day reachability, such as what is within 30 minutes by bus.
Preload into the API Serve a feed alongside the road dataset for the plugin.
QGIS MAP PLACEHOLDER
Transit service area: 30-minute pedestrian and bus reachability from a stop at 08:00, shaded by travel time, with the GTFS stops overlaid.
FIG 9A
netweevil
09 / 16

## Slide 10
BEYOND ROUTING
Agent-based traffic simulation included
Dispatch fleets of agents over the real network and watch congestion emerge. Greenshields or BPR flow, spillback queueing, live rerouting, zone effects, and temporal playback.
Fleets and demand Cars and bikes, peak or uniform departures, random or fixed OD.
Realistic flow Storage capacity, no-collision spillback, signal cycles.
Live rerouting Drivers escape jams on ranked alternatives mid-trip.
Zones and closures Slow zones, background load, event closures, even mid-run.
Temporal playback Frame-by-frame agent positions, animated in QGIS.
QGIS MAP PLACEHOLDER
Congestion snapshot at peak: edges coloured by speed ratio from free-flow to jam, with the city-centre slow zone outlined. Ideally a 2 to 3 frame strip for the carousel.
FIG 10A
netweevil
10 / 16

## Slide 11
DEFENSIBLE BY CONSTRUCTION
Reproducible and defensible by design
Every analysis writes a manifest that pins exactly what produced the result, so a number from a paper drafted months ago can be re-run and explained.
Source provenance
OSM extract path and hash, import timestamps, bundle IDs.
Profile hashes
The exact compiled cost model behind the run.
Software versions
Engine and algorithm version (edge_based_cch_v2).
Run metadata
Request, parameters, timing, captured rather than implied.
No hidden UI-only state. Anything you can configure serializes to file-backed config, request payloads, response metadata, or a manifest.
That is what turns a demo into an instrument you can publish from.
netweevil
11 / 16

## Slide 12
WHERE ANALYSTS WORK
QGIS-native, end to end
Point the plugin at a running API and drive everything from inside QGIS. Results come back as grouped, styled layers you can map immediately.
Click-to-run workflows Route, OD, matrix, service-area, transit, and simulation tabs.
Grouped layer output JSON, GeoJSON, GPKG, and simulation frames land organised.
Live simulation tab Watch a scenario play out frame by frame.
QGIS 3.28 to 4.99 Packaged as a normal installable plugin.
QGIS MAP PLACEHOLDER
QGIS screenshot: the netweevil plugin panel docked beside a styled route and service-area result, with the layer tree showing the grouped output.
FIG 12A
netweevil
12 / 16

## Slide 13
DIFFERENT TOOLS, DIFFERENT JOBS
Where each of these is the right call
OSRM
Fastest car routing at continental scale. Enormous query throughput, battle-tested, the reference for raw speed.
Valhalla
Production multimodal routing across the globe. Tiled, dynamic costing, mature, running real services today.
pgRouting
Routing inside your database. Arbitrary graph queries in SQL with deep PostGIS integration.
QNEAT3
Zero-setup network analysis inside QGIS. Open the plugin and go, with no services to run.
netweevil
My research niche. Explainable, tunable, reproducible analysis with simulation, all from one local binary.
If you need production routing or web-scale throughput, the others win, and that is by design. netweevil is not trying to take their place.
netweevil
13 / 16

## Slide 14
THE NICHE IT FILLS
What I could not get anywhere else, together
Any one of these exists somewhere. Having all of them in a single local engine aimed at research is the gap netweevil fills for me.
Every cost parameter explainable and tunable. from a readable, version-controlled file a reviewer can audit.
Reproducible run manifests. with source, profile, and version hashes pinned to every result.
Return shape you control per request. built for what an analysis needs, not for an app's render loop.
Exact routing with restrictions, plus simulation. shortest paths and agent-based traffic in the same tool.
All local, one binary. no database, tile server, or service to operate before you can ask a question.
netweevil
14 / 16

## Slide 15
STANDING ON SHOULDERS
Thank you to the open-source world
netweevil stands on a generation of open-source work. Without these projects, building something like this would not be thinkable.
DATA & STANDARDS
OpenStreetMap, the GTFS specification, MobilityData
ROUTING & RESEARCH
OSRM, Valhalla, pgRouting, OpenTripPlanner, the Contraction Hierarchies line, RoutingKit
GIS
QGIS and its community, QNEAT3 (Clemens Raffler)
SIMULATION
SUMO (Eclipse / DLR), MATSim
RUST ECOSYSTEM
Tokio and Axum, Serde, Rayon, the geo and OSM crates
AND EVERYONE
who writes papers, files issues, and shares code in the open
Thank you, all of you.
netweevil
15 / 16

## Slide 16
IN ONE BREATH
Not a faster OSRM.
Not a smaller Valhalla.
A local engine for the research case: where every parameter has to be explainable and tunable, every run reproducible, and the output shaped to whatever the analysis needs.
Built for my own pain points, the questions I kept needing to answer.
netweevil a local engine for network-analysis research, in Rust